## Slide 1: Model predictive control of compressor networks
Master’s Thesis: Midterm Presentation
Kathleen Jones
April 21, 2016

## Slide 2: Introduction
System: Compressor Surge
Causes:
  Increased pressure ratio/decreased mass flow
Effects:
    Unstable oscillations in mass flow through compressor
  Increased wear/maintenance cost
  Can cause safety concerns
Avoidance with recycle valve

## Slide 3: Introduction
Dedicated surge avoidance controller:
  Feedback loop for small disturbances
  Additional feedforward terms when certain thresholds are crossed
  Loop decoupling to separate it from pressure control/for multiple compressors
Disadvantages:
  Designed for gas turbines – don’t take advantage of quick response of electric drivers
  No explicit consideration of input constraints
  Interaction of multiple controllers
Current Industry Practices

## Slide 4: Introduction
Design and simulate MPC controllers for both parallel and serial networks of two compressors
  Needs to be computationally efficient
  Implemented by each compressor independently
Why MPC?
  Already been shown that MPC increases surge avoidance performance relative to traditional controllers for single compressors
  Can naturally handle interactions & input constraints
Thesis Goals

## Slide 5: Modelling
Single Compressor
States
Inputs
Disturbances
Input Volume
p1
OutputVolume
p2
Compressor
wc, mc
Recycle valve
urec, mr
Td
patm
u_in
u_out
patm

## Slide 6: Modelling
Single Compressor
Outputs
p2: Output pressure
SD: Surge distance

## Slide 7: Modelling
Grey-box modelling:
  Combination of parameter fitting and first principles
  Fix order of model based on first principles
  Use steady-state measurements to determine static model parameters
  Dynamic parameters taken equal to physical characteristics
Approach

## Slide 8: Modelling
Compressor Network
Discharge Tank
PD
patm
States
Inputs
Disturbances
u_tank

## Slide 9: Control
Linearized MPC
Prediction horizon: p = 100
Move horizon: u = 2
Augmented state includes:
  5 states per compressor
  Discharge tank pressure
  20-40 recycle valve delay states
  2 integrator states/compressor
Primary control objective: surge control of both compressors
Secondary control objectives:
  follow discharge pressure setpoint
  keep both output pressures equal (or objective from load-sharing controller)
Overview

## Slide 10: Control
Controller Setup
Procedure at each time step:
A posteriori state estimation
Linearize/discretize system around current operating point
Set up & solve QP
Apply optimal inputs
A priori state prediction
Observer & Linearization
QP Problem generation
QP solver & output
y
, A, B, C
QP
State Prediction
u

## Slide 11: Control
Objective:
Such that:
where is relative to the linearization point
Equations

## Slide 12: Control
4 inputs, 4 outputs
Likely too computationally expensive to implement in practice
Used as benchmark for other controllers
Outputs: SD and p2 for both compressors
Centralized Approach

## Slide 13: Control
Solve separate, smaller QP for each controller individually
  Each QP depends on inputs of other compressor – unknown
  Perform fixed # of iterations, updating the inputs at each step
Assume full state information available to both compressors (for now)
  Can also implement separate observers for each compressor
2 variants examined
  Cooperative: use single cost function for both compressors
  Non-cooperative: use separate cost function for each compressor
Decentralized Approach

## Slide 14: Control
Decentralized: QP Solver

## Slide 15: Control
Decentralized: Observer
A2,B2,C2
Observer 1
Observer 2
QP Generator1
QP Generator 2
A1,B1,C1
QP1
QP2

## Slide 16: Considerations
Tank Size
Cooperative unstable for
Non-cooperative unstable for
Cooperative unstable for
Non-cooperative unstable for
Assume steady-state and use prediction matrices to predict QP solution:

## Slide 17: Results
Output Disturbance

## Slide 18: Results
Input Disturbances

## Slide 19: Conclusion
Fine-tune controllers
Implement individual observers for each compressor
Quantify computational cost of each solution
  How many iterations of decentralized are still cheaper than centralized solution?
Compare results to industry standard (traditional control)
Repeat process for serial network
Future Work